## Slide 1: P8910 B0 I2C/I3C Path Filter Scan
Dec, 6th 2021

## Slide 2: Path1 – Spec I2C Path
I2C path filter test conditions |  | 
Item | Register | description
SWAB loading |  | 6A
SWC loading |  | 3A
SWD loading |  | 3A
Frequency |  | 100KHz, 400KHz, 600KHz, 800KHz, 1000KHz
IO voltage |  | 1.0V, 1.5V, 1.8V, 2.5V, 3.3V

## Slide 3: VIO 1.0V Full load VS 0A
 | VR Enable with IOUTAB=6A, IOUTC=3A, IOUTD=3A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=1.0V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | VR Enable with IOUTAB=0A, IOUTC=0A, IOUTD=0A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=1.0V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass

## Slide 4: VIO 1.5V Full load VS 0A
 | VR Enable with IOUTAB=6A, IOUTC=3A, IOUTD=3A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=1.5V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | VR Enable with IOUTAB=0A, IOUTC=0A, IOUTD=0A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=1.5V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass

## Slide 5: VIO 1.8V Full load VS 0A
 | VR Enable with IOUTAB=0A, IOUTC=0A, IOUTD=0A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=1.8V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | VR Enable with IOUTAB=6A, IOUTC=3A, IOUTD=3A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=1.8V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass

## Slide 6: VIO 2.5V Full load VS 0A
 | VR Enable with IOUTAB=6A, IOUTC=3A, IOUTD=3A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=2.5V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | VR Enable with IOUTAB=0A, IOUTC=0A, IOUTD=0A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=2.5V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass

## Slide 7: VIO 3.3V Full load VS 0A
 | VR Enable with IOUTAB=6A, IOUTC=3A, IOUTD=3A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=3.3V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | VR Enable with IOUTAB=0A, IOUTC=0A, IOUTD=0A |  |  |  | 
 | 100KHZ | 400KHZ | 600KHZ | 800KHZ | 1000KHZ
P8910B0 Data Path: I2C - Path1 Protocol: I2C No PEC V_Pullup=3.3V Dolphin3 + Option2 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass

## Slide 8: Path2 – Spec I3C Path
I3C path filter test conditions |  | 
Item | Register | description
SWAB loading |  | 6A
SWC loading |  | 3A
SWD loading |  | 3A
Frequency |  | 1MHz, 4MHz, 6MHz, 8MHz, 10MHz, 11MHz, 12MHz, 12.5MHz, 12.8MHz, 13MHz, 13.2MHz, 13.4MHz, 13.5MHz, 13.6MHz
IO voltage |  | 1.0V

## Slide 9: Path2:Scan I3C_PP_Filter
 |  | PEC Enable, VR Enable with IOUTAB=0A, IOUTC=0A, IOUTD=0A |  |  |  |  |  |  |  |  |  |  |  |  | 
 | PP_Filter 0xBC<3:0> | 1000KHZ | 4000KHZ | 6000KHZ | 8000KHZ | 10000KHZ | 11000KHZ | 12000KHZ | 12500KHZ | 12800KHZ | 130000KHZ | 13200KHZ | 13400KHZ | 13500KHZ | 13600KHZ
P8910B0 Data Path: I3C - Path2 Protocol: I3C PEC Enable I3C_OD_Freq=1000KHZ VOH/VIH=1.0V Dolphin3 is option2 | 0000 (2ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | 0001 (4ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | 0010 (6ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass
 | 0011 (8ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail
 | 0100 (10ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A
 | 0101 (12ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A
 | 0110 (14ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A
 | 0111 (16ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1000 (18ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1001 (20ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1010 (22ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1011 (24ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1100 (26ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1101 (28ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1110 (30ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, Fail 5/40000 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1111 (32ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A

## Slide 10: Path2:Scan I3C_PP_Filter
 |  | PEC Enable, VR Enable with IOUTAB=6A, IOUTC=3A, IOUTD=3A |  |  |  |  |  |  |  |  |  |  |  |  | 
 | PP_Filter 0xBC<3:0> | 1000KHZ | 4000KHZ | 6000KHZ | 8000KHZ | 10000KHZ | 11000KHZ | 12000KHZ | 12500KHZ | 12800KHZ | 130000KHZ | 13200KHZ | 13400KHZ | 13500KHZ | 13600KHZ
P8910B0 Data Path: I3C - Path2 Protocol: I3C PEC Enable I3C_OD_Freq=1000KHZ VOH/VIH=1.0V Dolphin3 is option2 | 0000 (2ns) | W&R 40000x, pass | W&R 40000x, Fail 1/40000 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 4000x, Fail 1/40000 | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 4000x, Fail 2/40000 | W&R 4000x, Fail 1/40000
 | 0001 (4ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, Fail 27/40000 | W&R 40000x, Fail 24/40001 | W&R 40000x, Fail 27/40002 | W&R 40000x, Fail 28/40002 | W&R 40000x, Fail 25/40003
 | 0010 (6ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail
 | 0011 (8ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail
 | 0100 (10ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 4000x, Fail 44/40000 | W&R 4000x, Fail 34/40000 | W&R 4000x, Fail 37/40000 | N/A | N/A | N/A | N/A | N/A
 | 0101 (12ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | W&R 100x, Fail | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A
 | 0110 (14ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 0111 (16ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, Fail 15/40000 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1000 (18ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1001 (20ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, Fail 1/40000 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1010 (22ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, Fail 24/40000 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1011 (24ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1100 (26ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1101 (28ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, Fail 7/40000 | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1110 (30ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | W&R 100x, Fail | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A
 | 1111 (32ns) | W&R 40000x, pass | W&R 40000x, pass | W&R 40000x, pass | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A

## Slide 11: Register Dump